## Slide 1: Challenges in the Assessment of Internal Exposure to European Spallation Source (ESS) Radionuclides
Belikse Ramljak

## Slide 2: What is internal dosimetry?
Photo from https://radiologykey.com/general-considerations-in-radiation-disaster-medicine/

## Slide 3
Medical treatments
Nuclear or radiological accidents
When do we care about internal dosimetry?
Usually a single radionuclide
Usually a mix of different radionuclides

## Slide 4: Why it is important?
It aids in assessment of:
Acute radiation effects
(almost instant damage to organs)
Long-term effects like cancer
Extract from GATE MC toolkit
simulation of activity and final absorbed dose to the rat
after injection of PET radiotracer, 18F-fluorodeoxyglucose (18F-FDG)
Arun Gupta et al 2019 Phys. Med. Biol. 64 095007

## Slide 5: Where do we use internal dosimetry results?
In the estimation of the effective dose received by the individual
In contamination monitoring strategies
In the design of medical treatment procedures
In the design of protection strategies for the public and workers during a nuclear or radiological accident

## Slide 6: How do we estimate internal contamination?
  Examination of excretion samples
Whole body counting
Image taken from SciencePhotoLibrary
Image taken from 3AW Melbourne

## Slide 7
With the help of…
Free software
Commercial software
Note: Simulation toolkits such as Geant4 are usually used solely for research purposes and usually only for a single radionuclide incorporation in the body!

## Slide 8
Nuclear /radiological emergency:
  Mix of radionuclides
  Radionuclides can be unevenly spread in different geographical areas
  Monitoring strategies have to be quick and effective
Focus today
Internal dose assessment challenges for European Spallation Source radionuclides

## Slide 9: European Spallation Source (ESS)
Roger Eriksson/ESS - https://dam.esss.lu.se/asset-bank
It will produce intense beams of neutrons for scientific research across physics, chemistry, biology, materials science, engineering, and energy research.

## Slide 10
These neutrons are then slowed down and guided to experimental stations
A high-energy proton beam (accelerated to 2 GeV) strikes a tungsten target.
The impact releases a large number of neutrons from the target atoms.
1
2
3
European Spallation Source (ESS)

## Slide 11
These neutrons are then slowed and guided to experimental stations
A high-energy proton beam (accelerated to 2 GeV) strikes a tungsten target.
The impact releases a large number of neutrons from the target atoms.
1
2
3
European Spallation Source (ESS)
Around 1000 radionuclides will be generated as by–products of spallation and activation reactions.

## Slide 12: Accident scenario –loss of cooling
Vytenis Barkauskas, Kristina Stenström, Prediction of the radionuclide inventory in the European Spallation Source target using FLUKA,
Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms,Volume 471,2020,Pages 24-32,
ISSN 0168-583X,
Image provided by ESS
Radionuclides are most likely to appear as oxide compounds.
Radionuclide releases are most likely to be fine aerosols (<10 µm).
An aerosol is a suspension of fine solid particles or liquid droplets in air or another gas. (Wikipedia)

## Slide 13: Route of intake
Inhalation
Ingestion
Wound

## Slide 14
where radionuclides will end up, geographically (atmospheric dispersion modelling);
how will they move through the body, where they will deposit (biokinetics modelling);
how we can detect them effectively (radiometry).
Which information we need to assess internal contamination?

## Slide 15
Challenges in atmospheric dispersion modelling
Environmental radioactivity and emergency preparedness, Mats Isaksson and Christopher L. Rääf, Series in Medical Physics and Biomedical Engineering, Taylor and Francis Group, 2017

## Slide 16
Challenges in atmospheric dispersion modelling
Averaging of wind speed
Simple turbulence model
Simple parameterization of deposition
No chemistry considerations
RIMPUFF (DTU) – used by Swedish Radiation Safety Authortiy

## Slide 17: FLEXPART

## Slide 18
Challenges in biokinetics modelling
Radionuclide | Half life | Dose coefficient (Sv/Bq)
148Gd | 71.1 y | 5.6E-8
187W | 23.9 h | 6.3E-10
172Hf | 1.87 y | 1.0E-9
182Ta | 115.0 d | 1.5E-9
178mHf | 31 y | 4.7E-9
Around 1000 radionuclides!
We need to make a selection!

## Slide 19
Alex Yartsev, Single and multiple compartment models of drug distribution | Deranged Physiology

## Slide 20
Lack of data (experiments) on gadolinium, tungsten, hafnium, and tantalum!

## Slide 21
Biokinetic model of gadolinium

## Slide 22
SENSITIVITY ANALYSIS OF THE ICRP BIOKINETIC MODEL PREDICTING THE ACTIVITY OF GD IN LUNGS AND 24-HOUR EXCRETION SAMPLESRamljak, B., Malusek, A., Eriksson Stenström, K. & Rääf, C., 2023 nov. 11, Kaunas University of Technology. Kaunas University of Technology, s. 55-59 (MEDICAL PHYSICS IN THE BALTIC STATES ).
More advanced model hopefully coming soon!

## Slide 23
I mentioned lack of data
Experimental investigation of dissolution of gadolinium in lungs

## Slide 24
Challenges in radiometry
Which equipment to select?
Which radionuclides we can monitor?
What is the good time period to monitor?

## Slide 25
Challenges in radiometry

## Slide 26: End slide, logotype only